GNU make
www.instigatedesign.com

---
Agenda
- Problem statement
- Solution overview
- makefile structure
- makefile syntax:
  - rules
  - variables
  - “include” directive
  - automatically generation of dependencies
  - built-in functions
  - template rules
  - special variables
- Examples

---
Problem statement : automatic build
- SW products build process involves primary and secondary files
- primary files are generated by user
  Ex: *.h, *.hpp, *.c, *.cpp, *.tex
- derived files are generated by programs based on primary files
  Ex: *.o, *.so, *.a, *.dvi, *.pdf
- generation process can involve many steps
- it has to be automated by some script

---
Problem statement : partial build
- in complex systems the generation process takes long time
- it can be speed up by regenerating only the files that are changed since last generation
- trying to do time-stamp based selective regeneration using manual scripting (e.g. shell) is tedious and error prone

---
Solution overview
- make tries to solve both these problems
- it provides means for build automation:
  - defining dependencies between files
  - defining rules to generate secondary files from primary files
- and it supports partial rebuild:
  - during build process it checks the time-stamps of files
  - regenerates only the files that are obsolete

---
Makefile structure
- make takes its rules from the makefile
- makefile contains
  - rules describing the dependencies
    Ex:
    file1.o : file1.cpp header1.hpp header2.hpp
  - commands that should be used to rebuild the dependent file
    Ex:
    g++ -c file1.cpp -o file1.o

---
Makefile syntax : rules
- makefile rule has following syntax:
  <target> : <prerequisites>
  <commands>
  - <target> is one or more identifiers (e.g target file name)
  - <prerequisites> is one or more identifiers (e.g prerequisite file name)
  - <commands> is a list of shell commands (/bin/sh)
  - if any of the targets is “older” than any of the prerequisites the <commands> will be executed

---
Makefile rules : example
file1.o : file1.cpp file1.hpp
cc -c file1.cpp -o file1.o
file2.o : file2.cpp file2.hpp file1.hpp
cc -c file2.cpp -o file2.o
program : file1.o file2.o
ld file1.o file2.o -o program

---
Makefile syntax : variables
makefile allows to define variables:
HEADERS := file1.hpp file2.hpp file3.hpp
SOURCE := file.cpp
TARGET := file.o
CC := gcc
Variables then can be used in rules and commands:
$(TARGET) : $(SOURCE) $(HEADERS)
$(CC) -c $(SOURCE) -o $(TARGET)

---
Makefile syntax : assignment
- There are two ways to assign value to the variable
  VARIABLE1 = value
  VARIABLE2 := value
  - the first way assumes re-evaluation of the RHS expression every time the variable is invoked
  - the second evaluates the RHS expression upon assignment
- Example:
  a = 1
  b = $a
  c := $a
  a = 2
  echo $b # should print 2
  echo $c # should print 1

---
Makefile syntax : built-in functions
- There is a set of helper string-processing functions making it easier to define variables. Ex:
  SOURCES := file1.cpp file2.cpp
  OBJECTS := $(subst .cpp,.o,$(SOURCES))
  - here “subst” allows to substitute all occurrences of “.cpp” by “.o” and makes it simpler and safer to define the variable “OBJECTS”
- Other helpful functions are:
  S = $(wildcard src/*.cpp)
  O = $(patsubst src/%.cpp,obj/%.o,$S)
  BASE_NAME = $(basename file.cpp) # = file
  NOT_DIR = $(notdir dir/file.cpp) # = file.cpp
  DIR_OBJ = $(addprefix dir/, $(OBJECTS))

---
Automatic generation of C++ file dependencies
Dependencies are caused by #include directive
each .o file depends on its corresponding .cpp and all headers directly or indirectly included by it:
file.o : file.cpp file.hpp ...
- there is a way to automatically extract that line:
  g++ -MM file.cpp will output dependency string
- to add it to the makefile, we can first send it to an external file
  g++ -MM file.cpp -o file.dep,
  and then include it from the makefile:
  -include file.dep
- use –, to avoid warning when the first time make runs

---
Automatic generation of C++ file dependencies
- the rule to create the *.dep file should also be put in the makefile
  file.dep :
  gcc -MM file.cpp -o file.dep
- but the *.dep file itself depends on same targets as the corresponding *.o file, therefore it makes sense to have them both in target list of the same rule:
  file.dep file.o : file.cpp file.hpp ...
- This can be achieved using -MT flag of the gcc:
  file.dep :
  gcc -MM file.cpp -MT “file.dep file.o” -o file.dep

---
Automatic generation of C++ file dependencies
Example:
SOURCES := file1.cpp file2.cpp
OBJECTS := $(patsubst %.cpp,%.o,$(SOURCES))
program : $(OBJECTS)
ld $(OBJECTS) -o program
file1.o :
g++ -c file1.cpp -o file1.o
file2.o :
g++ -c file2.cpp -o file2.o
file1.dep :
g++ -MM file1.cpp -MT “file1.dep file1.o” \
-o file1.dep
file2.dep :
g++ -MM file2.cpp -MT “file2.dep file2.o” \
-o file2.dep
-include file1.dep file2.dep

---
Makefile syntax : special variables
- The following special variables can be used within the command
  - $@ is the target
  - $< is the first prerequisite
  - $^ is list of all prerequisites
- Example:
file.o : file.cpp file.hpp
$@ is the file.o
$< is the file.cpp
$^ is the file.cpp file.hpp

---
Makefile syntax : implicit rules
- implicit rules are generic (template) rules to help with defining similar rules. E.g. instead of specifying a rule for each *.o file in the previous example, the following implicit rule can be used:
  %.o : %.cpp # rest is taken from .dep
  gcc -c $< -o $@
- similarly following implicit rule can be used to generate dependencies for all *.cpp files:
  %.dep : %.cpp # rest is taken from .dep
  gcc -MM $< -MT “$@ $(subst .dep,.o,$@)”-o $@

---
Using implicit rules and special variables
SOURCES := file1.cpp file2.cpp
OBJECTS := $(patsubst %.cpp,%.o,$(SOURCES))
DEPENDS := $(patsubst %.cpp,%.dep,$(SOURCES))
program : $(OBJECTS)
ld $^ -o $@
%.o : %.cpp
g++ -c $< -o $@
%.dep : %.cpp
g++ -MM %< -MT “$@ $(patsubst %.dep,%.o,$@)” -o $@
-include $(DEPENDS)

---
More complex example
SOURCES := $(wildcard src/*.cpp)
OBJECTS := $(patsubst src/%.cpp,obj/%.o,$(SOURCES))
DEPENDS := $(patsubst src/%.cpp,obj/%.dep,$(SOURCES))
bin/program : ./bin $(OBJECTS)
ld $(OBJECTS)-o bin/program
./bin:
mkdir -p bin
obj/%.o : src/%.cpp
g++ -c $< -o $@
obj/%.dep : src/%.cpp
g++ -MM %< -MT “$@ $(patsubst %.dep,%.o,$@)” -o $@
-include $(DEPENDS)